## Slide 1: PMIx: Process Management for Exascale Environments

## Slide 2: Agenda
State of the Community
  Ralph H. Castain (Intel)
Scaled Performance
  Aurelien Bouteiller (UTK)
PMIx Standards Document
  Josh Hursey (IBM)
Q&A

## Slide 3: Three Distinct Entities
PMIx Standard
  Defined set of APIs, attribute strings
  Nothing about implementation
PMIx Reference Library
  A full-featured implementation of the Standard
  Intended to ease adoption
PMIx Reference Server
  Full-featured “shim” to a non-PMIx RM
  Provides development environment
Standards Doc under development!

## Slide 4: Where Are We?
Launch scaling
  Wireup enhancements complete
  Fabric “instant on” enablement underway
Results
  Tracks spawn propagation time
  Exascale in < 5 seconds
  3rd party confirmation
EuroMPI 2017 Overview Article*
*extended version to be published

## Slide 5: PMIx Launch Sequence
*RM daemon, mpirun-daemon, etc.

## Slide 6: PMIx Launch Sequence
*RM daemon, mpirun-daemon, etc.

## Slide 7: Current Support (I)
Typical startup operations
  Put, get, commit, barrier, spawn, [dis]connect, publish/lookup
Tool connections
  Debugger, job submission, query
Generalized query support
  Job status, layout, system data, resource availability
Event notification
  App, system generated
  Subscribe, chained
  Preemption, failures, timeout warning, …
Logging
  Status reports, error output
Flexible allocations
  Release resources, request resources

## Slide 8: Current Support (II)
Network support
  Security keys, pre-spawn local driver setup
Obsolescence protection
  Automatic cross-version compatibility
  Container support
Job control
  Pause, kill, signal, heartbeat, resilience support (C/R coordination)
Async definition of process groups
  Rolling startup/teardown

## Slide 9
Courtesy of:
Víctor Sande Veiga
Supercomputing Center of Galicia
Should be all 
going forward
1.2.5
1.2.5
1.2.5
1.2.5
2.1
PMIX version

## Slide 10: Cross-Version Interoperability
PMIx v1.1.5
PMIx v1.2.5+
PMIx v2.0.3+
PMIx v2.1.x
PMIx v3.0.x
Any client/server
combination
Server >= Client

## Slide 11: In Pipeline
Network support
  Fabric topology and status, traffic reports, fabric manager interaction
MPI Sessions support
  Rolling startup/teardown
Generalized data store
  Distributed key-value storage
Security
  Obtain and validate credentials for application/SMS
Power directives
File system support
  Dependency detection
  Tiered storage caching strategies
Debugger/tool support++
  Automatic rendezvous
  Single interface to all launchers
  Co-launch daemons
  Access fabric info, etc.
Cross-library interoperation
  OpenMP/MPI coordination
Nearing completion
Ramping up
Idling

## Slide 12: Adoption
RMs
  SLURM, IBM’s Job Step Manager (JSM) complete
  Fujitsu underway, Altair ramping up
Libraries
  Open MPI, OSHMEM, SOS complete
  GASNet, ORNLshmem – in PR
  MPICH to come (1H2018?)
Tools
  Debugger integration under development

## Slide 13: Scalable Performance
Aurelien Bouteiller

## Slide 14: PMIx Launch Early Results
Comparing launch sequence of Open MPI with pmix vs aprun
ORNL Titan (Cray XK)
16 procs/node (8k ranks max)
4x speedup vs aprun

## Slide 15: PMIx Launch Early Results
MPI processes startup sequence:
  Modex Exchange (business card and NIC info)
  Fence
PMIx MPI processes startup sequence
  No Modex (PMIx provides business cards info from local RM)
  Fence unnecessary
In this experiment,
  MPI_Init fence is still present
  uGNI driver startup adds a significant latency (not present with e.g. EDR IB)
prun --npernode 16 -mca pmix_base_async_modex 1 –mca pmix_base_collect_data 0 -n 512*16 ./mpi_no_op

## Slide 16: PMIx Launch Early Results
In this experiment,
  MPI_Init fence is still present
  uGNI driver startup adds a significant latency (not present with e.g. EDR IB)
Try this at home! (and report back)
  Run Open MPI contrib/scaling/scaling.pl
  Will produce startup scalability data for
    Native launcher (e.g. Slurm, PBS, Alps)
    Open MPI `mpirun`
      With and without MPI_Init/Finalize fence
    PMIx `prun` with persistent daemons
      With and without MPI_Init/Finalize fence

## Slide 17: Side topic: Scalable Communication
17
PMIx Server
Ressource Manager
RM SCON
PMIx SCON
Vendor
Accelerated
REF
xcast
Resilient xcast
Network fabrics/drivers
SCON operations
External projects: not part of the PMIx specification
Mellanox: Hardware Accelerated Overlay
Intel/UTK: SCON: Scalable Communication Overlay Network
  Goals: scalable, generic, fault tolerant communication infrastructure for RTE systems
  New partners welcome 
SCON supply for communication features not provided from a supplier
  PMIx uses RM communication features, if available
  Similarly, RM uses internal communication features, if available
SCON will use vendor accelerated modules, when available
  Fallback to reference SCON operations when no vendor specific
Failure Detector (core function)
Reliable Broadcast (notifications)
Agreement (allgather/modex/fence)
MPI Agreement on Darter (Cray XC30)
Algorithms proven at the MPI level

## Slide 18: PMIx Standard Document
Josh Hursey

## Slide 19: PMIx Standard
Goal:
  Create a document that details the PMIx project goals, architecture, interfaces and semantics, and language bindings.
    Separate from the PMIx Reference Implementation.
  Ratify that document with the PMIx community.
    Open process to encourage broad participation.
Start with the interface from the PMIx Reference Implementation v2.0.
https://github.com/pmix/pmix-standard
Notes: Motivated by:
* an increasing number of venders providing PMIx – need a reference version to state compliance.
* an increasing number of RFC looking for a version to request minimal compliance for new systems.

## Slide 20: PMIx Standard
https://github.com/pmix/pmix-standard
Lots of work to do!
Requesting:
Assistance in crafting standard language,
Vigorous debate on semantics, and
Participation in the ratification process.

## Slide 21: PMIx Standard - Organization
Introduction to PMIx
  Overview, Goals, Architecture
PMIx Terms and Conventions
Data Structures, Types, Constants
  Includes: Reserved attributes, Keys
Initialization & Finalization
  Client, Server, Tool interfaces
Key/Value Management
  put, get, commit, fence
  (un)publish, lookup
Process Management
  spawn, (dis)connect, resolve_peers
Job Allocation Management
  Allocation request, process monitor
Event Handling
  (de)register_event, notify_event
Data Packing & Unpacking
  (un)pack, copy
PMIx Server Specific Interfaces
  setup_fork, (de)register_nspace
  pmix_server_module_t
Revisions, Acknowledgements
Bibliography
Index
https://github.com/pmix/pmix-standard

## Slide 22: PMIx Standard
Participation:
  File PRs against the GitHub repo
    https://github.com/pmix/pmix-standard
  Start a discussion on the PMIx community mailing list
    https://groups.google.com/forum/#!forum/pmix
  Join the weekly PMIx teleconference
    Thursday’s 3 pm (Eastern)
  The approval process is still being determined, but will likely match that of other HPC standardization bodies (e.g., MPI, OpenMP)
https://github.com/pmix/pmix-standard

## Slide 23: PMIx Standard
Questions for the community
  Is it important to have a v1.0 version of the standard to match the interface from the PMIx Reference implementation v1.x?
  The standard focuses on the C interface, how important are language bindings? Which additional languages should we focus on?
  What examples would you like to see in the standard to help illustrate how PMIx should be used?
  How should the standardization ratification process be structured? What determines a voting member of the community?
https://github.com/pmix/pmix-standard

## Slide 24: PMIx Standard
New interfaces & Semantic changes for discussion
  A PMIx server can return PMIX_ERR_NOT_SUPPORTED if a given attribute to, for example, PMIx_Get() is not supported. We do not have an interface for the PMIx client to query this information so they know in advance what attribute is supported.
    Is this functionality that would be useful to PMIx clients/applications?
    In what form should we provide that query mechanism?
      PMIx_Query_supported_attributes(…)
      Special PMIx attribute PMIX_PROBE_SUPPORT passed with the attribute?
      ???
https://github.com/pmix/pmix-standard

## Slide 25: PMIx Standard
New interfaces & Semantic changes for discussion
  Attributes can be required or not. What should be the default?
    Currently we default to not required
  Other suggestions?
https://github.com/pmix/pmix-standard

## Slide 26: Agenda
State of the Community
  Ralph H. Castain (Intel)
Scaled Performance
  Aurelien Bouteiller (UTK)
PMIx Standards Document
  Josh Hursey (IBM)
Q&A
Reminder:
Enhanced launch scaling talk
SLURM booth @ 2pm