## Slide 1: Process Management Interface – Exascale

## Slide 2: PMIx – PMI exascale
Collaborative open source effort led by Intel, Mellanox Technologies, IBM, Adaptive Computing, and SchedMD.
New collaborators are most welcome!

## Slide 3: Motivation
Exascale launch times are a hot topic
  Desire: reduce from many minutes to few seconds
  Target: O(106) MPI processes on O(105) nodes thru MPI_Init in < 30 seconds
New programming models are exploding
  Driven by need to efficiently exploit scale vs. resource constraints
  Characterized by increased app-RM integration

## Slide 4: Objectives
Establish an independent, open community
  Industry, academia, lab
Standalone client/server libraries
  Ease adoption, enable broad/consistent support
  Open source, non-copy-left
  Transparent backward compatibility
Support evolving programming requirements
Enable “Instant On” support
  Eliminate time-devouring steps
  Provide faster, more scalable operations

## Slide 5: Active Thrust Areas
Launch scaling
Flexible allocation support
I/O support
Advanced spawn support
Network support
Power management support
Fault tolerance and prediction
Workflow orchestration

## Slide 6: Motivation
Exascale launch times are a hot topic
  Desire: reduce from many minutes to few seconds
  Target: O(106) MPI processes on O(105) nodes thru MPI_Init in < 30 seconds
New programming models are exploding
  Driven by need to efficiently exploit scale vs. resource constraints
  Characterized by increased app-RM integration

## Slide 7: Launch Process
Allocation definition sent to affected root-level daemons
  Session user-level daemons are started and wireup
Application launch command sent to session daemons
  Daemons spawn local procs
Procs initialize libraries
  Setup required bookkeeping, identify their endpoints
  Publish all information to session key-value store, and barrier
Session daemons circulate published values
  Variety of collective algorithms employed
  Release procs from barrier
Procs complete initialization
  Retrieve endpoint info for peers

## Slide 8
Launch
Initialization
Exchange MPI contact info
Setup MPI structures
barrier
mpi_init completion
barrier
MPI_Init
MPI_Finalize
RRZ, 16-nodes, 8ppn, rank=0
Time (sec)

## Slide 9: Launch Process
Allocation definition sent to affected root-level daemons
  Session user-level daemons are started and wireup
Application launch command sent to session daemons
  Daemons spawn local procs
Procs initialize libraries
  Setup required bookkeeping, identify their endpoints
  Publish all information to session key-value store, and barrier
Session daemons circulate published values
  Variety of collective algorithms employed
  Release procs from barrier
Procs complete initialization
  Retrieve endpoint info for peers
Obstacles to scalability

## Slide 10: What Is Being Shared?
Job Info (~90%)
  Names of participating nodes
  Location and ID of procs
  Relative ranks of procs (node, job)
  Sizes (#procs in job, #procs on each node)
Endpoint info (~10%)
  Contact info for each supported fabric
Known to local RM daemon
Can be computed for many fabrics

## Slide 11
Launch
Initialization
Exchange MPI contact info
Setup MPI structures
barrier
mpi_init completion
barrier
MPI_Init
MPI_Finalize
RRZ, 16-nodes, 8ppn, rank=0
Time (sec)
Stage I
Provide method for RM to share job info
Work with fabric and library implementers to compute endpt from RM info

## Slide 12
Launch
Initialization
Exchange MPI contact info
Setup MPI structures
barrier
mpi_init completion
barrier
MPI_Init
MPI_Finalize
RRZ, 16-nodes, 8ppn, rank=0
Time (sec)
Stage II
Add on 1st communication
(non-PMIx)

## Slide 13
Launch
Initialization
Exchange MPI contact info
Setup MPI structures
barrier
mpi_init completion
barrier
MPI_Init
MPI_Finalize
RRZ, 16-nodes, 8ppn, rank=0
Time (sec)
Stage III
Use HSN+Coll

## Slide 14: Current Status
Stage I-II
Stage III (projected)

## Slide 15: Can We Go Faster?
Remaining startup time primarily consumed by
  Positioning of application binary
  Loading dynamic libraries
  Bottlenecks: global file system, IO nodes
Stage IV: Pre-Positioning
  WLM extended to consider retrieval, positioning times
  Add NVRAM to rack-level controllers and/or compute nodes for staging
  Pre-cache in background (during epilog, at finalize, …)

## Slide 16: What Gets Positioned?
Historically used static binaries
  Lose support for scripting languages, dynamic programs
Proposal: containers
  Working with Shifter & Singularity groups
  Execution unit: application => container (single/multi-process)
  Detect containerized application at job submission
  Auto-containerize if not (past history of library usage)? Layered containers?
Provisioning
  Provision when base OS is incompatible with container (Warewulf)

## Slide 17: How Low Can We Go?
Launch/wireup as fast as executables can be started
MPI+: Rolling starts, dynamic communicators

## Slide 18: Motivation
Exascale launch times are a hot topic
  Desire: reduce from many minutes to few seconds
  Target: O(106) MPI processes on O(105) nodes thru MPI_Init in < 30 seconds
New programming models are exploding
  Driven by need to efficiently exploit scale vs. resource constraints
  Characterized by increased app-RM integration

## Slide 19: Changing Needs
Notifications/response
  Errors, resource changes
  Negotiated response
Request allocation changes
  shrink/expand
Workflow management
  Steered/conditional execution
QoS requests
  Power, file system, fabric
Multiple, use-specific libs?
(difficult for RM community to support)
Single, multi-purpose lib?

## Slide 20: Scalability
Memory footprint
  Distributed database for storing Key-Values
    Memory cache, DHT, other models?
  One instance of database per node
    "zero-message" data access using shared-memory
Launch scaling
  Enhanced support for collective operations
    Provide pattern to host, host-provided send/recv functions, embedded inter-node comm?
  Rely on HSN for launch, wireup support
    While app is quiescent, then return to mgmtEth

## Slide 21: Flexible Allocation Support
Request additional resources
  Compute, memory, network, NVM, burst buffer
  Immediate, forecast
  Expand existing allocation, separate allocation
Return extra resources
  No longer required
  Will not be used for some specified time, reclaim (handshake) when ready to use
Notification of preemption
  Provide opportunity to cleanly pause

## Slide 22: I/O Support
Asynchronous operations
  Anticipatory data fetch, staging
  Advise time to complete
  Notify upon available
Storage policy requests
  Hot/warm/cold data movement
  Desired locations and striping/replication patterns
  Persistence of files, shared memory regions across jobs, sessions
  ACL to generated data across jobs, sessions

## Slide 23: Spawn Support
Staging support
  Files, libraries required by new apps
  Allow RM to consider in scheduler
    Current location of data
    Time to retrieve and position
    Schedule scalable preload
Provisioning requests
  Allow RM to consider in selecting resources, minimize startup time due to provisioning
  Desired image, packages

## Slide 24: Network Integration
Quality of service requests
  Bandwidth, traffic priority, power constraints
  Multi-fabric failover, striping prioritization
  Security requirements
    Network domain definitions, ACLs
Notification requests
  State-of-health
  Update process endpoint upon fault recovery
Topology information
  Torus, dragonfly, …

## Slide 25: Power Control/Management
Application requests
  Advise of changing workload requirements
  Request changes in policy
  Specify desired policy for spawned applications
  Transfer allocated power to specifed job
RM notifications
  Need to change power policy
    Allow application to accept, request pause
  Preemption notification
Provide backward compatibility with PowerAPI

## Slide 26: Fault Tolerance
Notification
  App can register for event notifications, incipient faults
    RM-app negotiate to determine response
  App can notify RM of errors
    RM will notify specified, registered procs
Rapid application-driven checkpoint
  Local on-node NVRAM, auto-stripe checkpoints
  Policy-driven “bleed” to remote burst buffers and/or global file system
Restart support
  Specify source (remote NVM checkpoint, global filesystem)
  Location hints/requests
  Entire job, specific processes

## Slide 27: Fault Prediction: Methodology
Exploit access to internals
  Investigate optimal location, number of sensors
  Embed intelligence, communications capability
Integrate data from all available sources
  Engineering design tests
  Reliability life tests
  Production qualification tests
Utilize learning algorithms to improve performance
  Both embedded, post process
  Seed with expert knowledge

## Slide 28: Fault Prediction: Outcomes
Continuous update of mean-time-to-preventative-maintenance
  Feed into projected downtime planning
  Incorporate into scheduling algorithm
Alarm reports for imminent failures
  Notify impacted sessions/applications
  Plan/execute preemptive actions
Store predictions
  Algorithm improvement

## Slide 29: Workflow Orchestration
Growing range of workflow patterns
  Traditional HPC: bulk synchronous, single application
  Analytics: asynchronous, staged
  Parametric: large number of simultaneous independent jobs
Ability to dynamically spawn a job
  Need flexibility – min/max size, rolling allocation, …
  Events between jobs and cross-linking of I/O
  Queuing of spawn requests
Tool interfaces that work in these environments

## Slide 30: Workload Manager: Job Description Language
Complexity of describing job is growing
  Power, file/lib positioning
  Performance vs capacity, programming model
  System, project, application-level defaults
Provide templates?
  System defaults, with modifiers
    --hadoop:mapper=foo,reducer=bar
  User-defined
    Application templates
    Shared, group templates
  Markup language definition of behaviors, priorities
30 yrs

## Slide 31: PMIx Roadmap
2014
1/2016
1.1.3
Full PMIx reference server in OpenMPI
Client library includes all APIs used by MPI
SLURM server integration complete

## Slide 32: PMIx Roadmap
2014
1/2016
1.1.3
2Q2016
2.0.0
Support for new APIs:
Event notification
Flexible allocation
System query
Scaling support:
Shared memory datastore

## Slide 33: PMIx Roadmap
2014
1/2016
1.1.3
2Q2016
2.0.0
3Q2016
RM Production Release*
2.1
Fabric manager integration
Topology info
Event reports
Process endpoint updates
File system integration
Pre-position requests
4Q2016
*SLURM, IBM, Moab, PBSPro,…

## Slide 34: Bottom Line
We now have an interface library to support application-directed requests
Community is working to define what they want to do with it
For any programming model
MPI, OSHMEM, PGAS,…